## Slide 1: Control Design and Implementation of a Small-Scale Autonomous Hovercraft
Ryan Mackay
Joshua Bevan
Nicholas Lutz
Mario Stamatiou
University of Massachusetts Lowell
James B. Francis College of Engineering
Department of Mechanical Engineering Capstone

## Slide 2: Introduction
Hovercrafts present a unique control challenge
  It is an under-actuated system
    3 DOF of motion, 2 DOF of control
    Requires optimization techniques to operate
The objective was to develop a robust control of the platform
  Using GPS and inertial data provided by the IMU
  Autonomously navigate between set waypoints

## Slide 3: Overview
Hovercraft Platform
  Theory
  Mechanical Systems
  APM
  Design Methodology
Control Algorithm
  Concepts
  Inertial frame and body frame-dynamics of hovercraft
  Inertial frame and body frame-kinematics of hovercraft
  Set Point detection-turning
  Setpoint detection-cruising
Implementation
  Procedures and Methods for Design
  Code Generation
  Ground Control
Results and Analysis
  Non-Optimized Track Test
  Cross Track Error Optimized Track Test
  Steering/Crosstrack Optimized & Box Test
  Stability Dependence on Initial Conditions
Further Study
Special Thanks

## Slide 4: Theory
Lift Fan supplies air pressure filling the cavity and inflating the skirt
Once the air pressure equals the weight of the hovercraft the hover craft lifts and air escapes from the outlet ducts.
The escaping air creates a thin layer of air between the skirt and ground allowing the hovercraft to float over the ground.
Hovercraft Platform

## Slide 5: Mechanical Systems
Modified model hovercraft
Servo driven rudder system.
Single propeller thrust and lift fans.
Powered by 2000mAh NiMH and 3200mAh 4S LiPo batterys.
Hovercraft Platform

## Slide 6: Electronics
APM
GPS
APM 2.5+ Assembled (Top entry) with 915Mhz (US) Telemetry Set
3-axis gyro, accelerometer and magnetometer, along with a high-performance barometer
Onboard 4 MP Dataflash chip for automatic datalogging
Arduino Compatible
3DR GPS uBlox LEA-6
5 Hz update rate
25 x 25 x 4 mm ceramic patch antenna
38 x 38 x 8.5 mm total size, 16.8 grams.
Hovercraft Platform

## Slide 7: Design Methodology
Steering Mechanism
  Rudder
    More challenging control scheme due to parasitic thrust
  Differential Thrust
    Capability of turning in place, allowing more sophisticated control
Lift Mechanism
  Flow Directing Duct
    Uses a single fan, but requires thrust at all times during operation
  Separate Lift Fan
    Allows low thrust without losing lift
Microcontroller/ IMU
  PX4
    More powerful processor
  APM
    More thoroughly documented source code and tutorials
Hovercraft Platform

## Slide 8
  Concepts that were applied for development of control algorithm
    Uses of Inertial frame and body frame for dynamic and kinematic analysis
    The hovercraft is an under-actuated vehicle since there are three degrees of freedom and only two available control inputs.
    Line of sight for detecting setpoints while turning and cruising
    Control theory application
Control Algorithm

## Slide 9: Inertial body frame dynamics
Both Inertial frame and body-fixed frame are used for development of control algorithm
Inertial frame assumes a fixed origin. The Earth is assumed to be the origin of the inertial reference frame
Coordinates are defined in inertial reference frame
Force, moment velocity and acceleration are defined in body-fixed frame
East
: North
: forward direction on body-fixed frame ; :surge
: right direction on body-fixed frame; : sway
: angular velocity
Control Algorithm

## Slide 10: Inertial frame and body frame-kinematics
Re-direction of thrust from rudder creates and
generates a moment causing the hovercraft to turn;
Amount of thrust is expressed as a percentage relative to the maximum
From Newton’s 2nd Law
(assuming sway and kinetic friction are negligible)
=>
Control Algorithm

## Slide 11: Set Point detection-turning
Hovercraft relies on line of sight to identify setpoint
The following condition has to be satisfied to identify setpoint
where ε is a waypoint angle that bisects
: angle of hovercraft in inertial frame w.r.t line of setpoint
ψ: angle of hovercraft in inertial frame w.r.t surge component
(: setpoint coordinates
; ψr=
Control Algorithm

## Slide 12: Setpoint detection-cruising
Once alignment is achieved the hovercraft translates until ( is reached. The distance ρ is given by:
A waypoint radius R is defined to let the board know when the hovercraft has reached the setpoint.
The point will have been reached under the condition
Control Algorithm

## Slide 13: Control Algorithm
The goal of the control algorithm is to adjust the amount of thrust and yaw while the hovercraft is approaching the set point
For turning:
T%=
∆%=-Kψeψ-Krr
For cruising:
T%=Kρρ-Kuu
∆%=-Kψ’eψ-Kr’r
and so a single PID loop cannot be used, so
=0,=0
Control algorithm uses a combination of proportional control
Coefficients Kρ Ku and can be accessed in the software of ArduRover
Implemented Algorithm

## Slide 14: Procedures and Methods for Design
Implementation

## Slide 15: Methods for Design
1|PID ρ_pid, u_pid, Ψ_pid, r_pid;
2|if ( |bearing_error| < max angle for cruise )
3| Target_speed = cruise_speed + ρ_pid( distance_to_waypoint, kp=Kρ , ki=0, kd=0 )
4| Target_speed = Target_speed + ρ_pid( ground_speed, kp=Ku , ki=0, kd=0 )
5|else
4| Target_speed = cruise_speed
5|T% = calc_throttle( Target speed )
6|Limit T%min ≤ T% ≤ T%max
7|∆% = Ψ_pid( sin(bearing_error), kp=Kψ , ki=0, kd=0 )
8|∆% = r_pid( omega.z, kp=Kr , ki=0, kd=0 )
9|∆% = (∆%)(cruise_speed/ground_speed)
Pseudo Code implementation of Control Algorithm
  Differentiates between turning and cruising
  Because in we use the sum of P’s rather than full PID’s.
    Use generic PID function for generality
Implementation

## Slide 16: Generated Code
Implementation

## Slide 17
Generated Code
Implementation

## Slide 18: Ground Control
Implementation

## Slide 19: Non-Optimized Track Test
Results and Analysis

## Slide 20: Cross-Track Error Optimization
Results and Analysis

## Slide 21: Steering/Crosstrack Optimization
Results and Analysis

## Slide 22: Stability Dependence on Initial Conditions
Results and Analysis

## Slide 23: Further Study
Investigate terrain sensing
  Infer terrain properties from inertial data and adjust lift in response
Explore path optimization
  All waypoints are available at the start of flight
  It should be possible to look forward in the path and plan actions beforehand
Develop controls to be used with a craft using differential thrust
  Decoupling turning moment and thrust allows path optimization to be explored
Use sonar capabilities for obstacle avoidance
  ArduRover software has the capability of doing obstacle avoidance
  Adding a sonar module, autonomous navigation could be improved

## Slide 24: Special Thanks
We would like to acknowledge the efforts of Professor Raptis in acting as our capstone advisor. His contributions to our understanding of the theoretical and practical implementations of the control algorithm were invaluable. We would like to thank all the professors of the Mechanical Engineering Department for providing us the knowledge that was applied in successfully achieving the goal of this project. Additionally, we would like to thank RC Buyer’s Warehouse of Nashua, NH for providing advice on equipment selection.